## Slide 1
2026.4.21
陈信均 何衍宁
Freezing Time and Slicing Space
Ultrafast Laser For Bioimagine

## Slide 2
Content
Background
Temporal Resolution
Spatial Resolution
Conclusions
1
2
3
4
2

## Slide 3
Background
Time: Capturing Molecular Dynamics
Space: Macroscopic 3D Imagine
3
Bottlenecks in Traditional Methods
Standard detectors are slower than molecular relaxation
Clinical markers like Melanin are non-fluorescent
Distinguishing between substances is difficult.
Traditional fundus cameras provide only 2D surface observation
High-NA lenses have a very shallow focal depth
Deep anatomical layers remain blurred under conventional optical methods

## Slide 4
Background
Time and Frequency Differences
Ultrafast Laser vs CW
Fourier Transform Limit:
Ultra-short :
Breaking the bottleneck of electronic shutter technology: Pump-Probe
Ultra-broad
Extremely short spatial coherence length: OCT
Huge instantaneous power

## Slide 5
Temporal Resolution
5
Technical Principle
Time: Capturing Molecular Dynamics
Pump Pules: Using strong pulses to instantaneously induce excited states in molecules
Probe Pulse: The weak pulse arrives after a delay, and is responsible for "reading" the transient absorption change

## Slide 6
Temporal Resolution
6
Technical Principle in One Single Molecule
The transition of TTT and TTC
Ultrafast Transition: Captures the TTT to TTC conversion within 200 fs via coherent vibrational dynamics.
Full Relaxation: Tracks the final decay of the product back to the ground state over 160 ps.
The change of absorption Peak and Time information could be recorded by Probe.
Pump
J. Chem. Phys. 140, 244301 (2014)

## Slide 7
Temporal Resolution
7
Technical Principle in the Whole System
Changing The Time Delay
Electronic timing circuits cannot resolve femtosecond-scale events.
The Optical Solution: Modulating the travel distance of the Probe pulse via a motorized translation stage.
Stage displacement,
c: Speed of light )
L

## Slide 8
8
The Diagnostic Dilemma of Traditional Histopathology
Both malignant and benign lesions can exhibit dermal melanocytes (真皮黑素细胞).
Lacking chemical contrast, pathologists must rely on subjective architectural evaluation, leading to high false-positive rates and 14% diagnostic discordance.
Sci. Transl. Med. 3, 71ra15 (2011)
Temporal Resolution
Malignant Melanoma (黑色素瘤) (Dermal melanocytes present)
Benign Nevus (黑色素痔) (Dermal melanocytes also present)

## Slide 9
9
Differentiating Melanoma (黑色素瘤) from Melanocytic Nevi (黑色素痔)
The Baseline (0 fs): At zero delay, both melanins exhibit a negative signal (Ground-state depletion).
The Contrast Window (>300 fs):
Pheomelanin (褐黑素): Negative, extremely short-lived decay.
Eumelanin (真黑色素): Positive, long-lived excited-state absorption (ESA).
Sci. Transl. Med. 3, 71ra15 (2011)
Temporal Resolution
Pump-Probe Signals

## Slide 10
10
Differentiating Melanoma (黑色素瘤) from Melanocytic Nevi (黑色素痔)
Sci. Transl. Med. 3, 71ra15 (2011)
Temporal Resolution
Pump-Probe Signals
Malignant Melanoma (恶性黑色素瘤): Demonstrates intense positive signals at 300 fs, indicating a high concentration of Eumelanin (真黑色素)
Benign Nevus (良性痣): Exhibits an absence of signal at 300 fs, confirming the lesion is almost entirely composed of Pheomelanin (褐黑素).

## Slide 11
Spatial Resolution
11
OCT(Optical Coherence Tomography) vs. Ultrasound
Performance Indicator | OCT | Clinical High-Frequency Ultrasound
Detection Medium | Near-Infrared (Low Coherence) | Sound Waves (10-50 MHz)
Axial Resolution |  | ~100
Imaging Depth | 1 ~ 3 mm | 30 ~ 100 mm
Performance Indicator | OCT | Clinical High-Frequency Ultrasound
Detection Medium | Near-Infrared (Low Coherence) | Sound Waves (10-50 MHz)
Axial Resolution |  | 
Imaging Depth | 1 ~ 3 mm | 30 ~ 100 mm
OCT, often referred to as "optical ultrasound“, strikes a perfect balance between resolution and depth of penetration.
High Resolution Imaging in Microscopy and Ophthalmology: New Frontiers in Biomedical Optics, edited by J. Roland, J. P. Rolland, and J. Jannick (Springer Nature, 2014).

## Slide 12
Spatial Resolution
12
Low-Coherence Interferometry
OCT：Core Principle
Low-coherence interferometry via a Michelson interferometer geometry
Interference occurs only when the optical path difference is strictly within the coherence length
Axial Resolution
(Wider bandwidth Higher resolution)
Advantages of Ultrafast Lasers:
According to the Fourier transform limit, a femtosecond pulse inherently possesses an extremely broad spectral bandwidth.

## Slide 13
13
OCT：Technical Evolution
SD-OCT：Spectral-Domain OCT
Eliminates mechanical reference arm scanning
High Resolution Imaging in Microscopy and Ophthalmology: New Frontiers in Biomedical Optics, edited by J. Roland, J. P. Rolland, and J. Jannick (Springer Nature, 2014).
Coherent information from all depths is acquired in the frequency domain using a spectrometer
Phase Stability
Spatial Resolution

## Slide 14
14
OCT Applications：Structural imaging
Optical Biopsy of Retinal Layers
High-sensitivity resolution of stratified microstructures of the retina
using the ultra-broad spectrum of ultrafast lasers.
Spatial Resolution

## Slide 15
15
Optical Biopsy of Retinal Layers
OCT Applications：Structural imaging
A patient with
diabetic macular edema
A patient with choroidal neovascularization resulting from age-related macular degeneration (AMD)
A patient with neovascular
AMD with extensive subretinal hyperreflective material
Spatial Resolution
DME diagnosis: Real-time assessment of tissue fluid accumulation and cystic edema in areas such as the inner nuclear layer.
Drusen Identification: Precisely captures the minute bumps caused by the glass film light spot (Drusen) beneath the RPE layer.
Leakage monitoring: Observe the accumulation of subretinal high reflectivity material (SHRM), which is usually an important marker of choroidal neovascularization (CNV) and its activity.
C. De Fauw et al., Nat. Med. 24, 1342 (2018)

## Slide 16
16
OCT Applications：Commercialization
Zeiss Cirrus 5000
Spatial Resolution
Heidelberg Spectralis
Mocean 4000
Successful market entry of OCT devices.

## Slide 17
17
Diagnostic Science
Conclusions
Ultrafast laser technology is an important tool of modern label-free biomedical diagnostics.
Temporal Domain: Transient Dynamics
The Pump-Probe method turns spatial distance into high time resolution. It helps us capture the fast process of heat loss at the molecular level.
Spatial Domain: 3D Anatomy
OCT uses the features of ultrafast lasers to produce 3D images with extremely high resolution. Unlike traditional tools, it can show deep details clearly without touching the body.
Future
The combination of deep learning and functional OCT/Pump-Probe will provide a new imaging tool. It will further improve the quality of medical pictures and offer more help in clinical medicine.

## Slide 18
18
References
[1] H.A. Haus, Mode-locking of lasers, IEEE Journal of Selected Topics in Quantum Electronics 6(6) (2000) 1173-1185.https://doi.org/10.1109/2944.902165
[2] A.H. Zewail, Femtochemistry: Atomic-Scale Dynamics of the Chemical Bond, The Journal of Physical Chemistry A 104(24) (2000) 5660-5694.https://doi.org/10.1021/jp001460h
[3] D. Huang, E.A. Swanson, C.P. Lin, J.S. Schuman, W.G. Stinson, W. Chang, M.R. Hee, T. Flotte, K. Gregory, C.A. Puliafito, J.G. Fujimoto, Optical Coherence Tomography, Science 254(5035) (1991) 1178-1181.https://doi.org/doi:10.1126/science.1957169
[4] I.R. Piletic, T.E. Matthews, W.S. Warren, Probing Near-Infrared Photorelaxation Pathways in Eumelanins and Pheomelanins, The Journal of Physical Chemistry A 114(43) (2010) 11483-11491.https://doi.org/10.1021/jp103608d
[5] W. Min, S. Lu, S. Chong, R. Roy, G.R. Holtom, X.S. Xie, Imaging chromophores with undetectable fluorescence by stimulated emission microscopy, Nature 461(7267) (2009) 1105-1109.https://doi.org/10.1038/nature08438
[6] T.E. Matthews, I.R. Piletic, M.A. Selim, M.J. Simpson, W.S. Warren, Pump-probe imaging differentiates melanoma from melanocytic nevi, Sci Transl Med 3(71) (2011) 71ra15.https://doi.org/10.1126/scitranslmed.3001604
[7] N. Nishizawa, Wideband ultrafast fiber laser sources for OCT and metrology, Journal of Physics B: Atomic, Molecular and Optical Physics 49(18) (2016) 182003.https://doi.org/10.1088/0953-4075/49/18/182003
[8] P. Chen, Z. Long, Q. Cheng, M. Song, W. Wang, R. Liu, Z. Zhang, K. Xia, Z. Yang, L. Qian, S. Bai, X. Wang, P. Yang, P. Xu, E.S. Yousef, R. Wang, On-Chip Supercontinuum Generation Pumped by Short Wavelength Fiber Lasers, Photonics, 2024, p. 440.10.3390/photonics11050440.

## Slide 19
THANKS FOR ATTENTION！