## Slide 1
EE104 Fundamentals of Electric Circuits (Supplementary)
Jun MA | 马俊
E-mail: maj3@sustech.edu.cn
南方科技大学-工学院-电子与电气工程系-PN Lab

## Slide 2
1. A rotating rod (a)
A useful way to think of a cosine wave is as the projection of a rotating rod onto the horizontal axis.
For a unit-length rod, the projection has length cos θ.
If the rod is rotating at a speed of f revolutions per second, then θ increases uniformly with time: θ = 2πft.
Therefore the projection is cos(2πft) or cos(ωt).
A complex number that is used to represent a sinusoidal voltage or current is called a phasor.

## Slide 3
1. A rotating rod (b)
Based on the rotating rod model, the only difference between cos and sin is the starting position of the rod.
sin(2πft) lags cos(2πft) by π/2, because it peaks at ¼ of a cycle.
v1(t) = cos(2πft)
v2(t) = sin(2πft)
v2(t) = cos(2πft – π/2)

## Slide 4
2. Phasors 1 (a)
1. If the rod has length A and starts at an angle φ then the projection onto the horizontal axis is
  Acos(ωt + φ) = Acosφ cos(ωt) – Asinφ sin(ωt)
  Lex X = A cosφ and Y = A sinφ
  Acos(ωt + φ) = Xcos(ωt) – Ysin(ωt)
2. At t = 0, the tip of the rod has coordinates
  (X, Y) = (Acosφ, Asinφ)
3. If plane is a complex plane, the complex number X + jY corresponding to the tip of the rod at t = 0 is called a phasor.
4. The magnitude of the phasor, , gives the amplitude (peak value) of the sine wave.
5. The argument of the phasor, φ, gives the phase shift relative to the cos(ωt).

## Slide 5
2. Phasors 1 (c)
Phasor domain
Time domain
v1(t) = cos(ωt)
V1 = 1, f = 50 Hz
V2 = –j, f = 50 Hz
v2(t) = sin(ωt)
V = X + jY
V = A
v(t) = Xcos(ωt) – Ysin(ωt)
v3(t) = Acos(ωt + )
A phasor represents an entire waveform (encompassing all time) as a single complex number. We assume the frequency, f, is known.
A phasor does not vary with time.

## Slide 6
3. phasors 1 (d)
At a certain time t:
At time goes by

## Slide 7
3. phasors 2 (a)

## Slide 8
3. phasors 2 (a)
ω
Vectors 向量
Phasors 相量
Vectors are stationary and pointing toward a point on a plane
Phasors is a complex number, and “a vector rotating at a certain frequency ω on a complex plane”.
0
x
y
Re
Im
0

## Slide 9
3. phasors 2 (b)
ω
Phasors 相量
Phasors is vector rotating at a certain frequency ω on the complex plane.
Re
Im
0
(1) At t = 0: (to define the vector)
(2) For t 0: (to make the vector rotate)

## Slide 10
3. phasors 2 (d)
Time domain, the same frequency
v1(t) = 1.5sin(t)
v2(t) = -cos(t)
To calculate in time domain:
v (t) = v1(t) + v2(t) = 1.5sin(t) – cos(t)

## Slide 11
3. phasors 2 (e)
Time domain
Phasor domain

## Slide 12
3. phasors 2 (f)
Time domain
Phasor domain
v1(t) = 1.5sin(t)
v2(t) = -cos(t)
v1(t) ⇒ V1ejωt v2(t) ⇒ V2ejωt
V1e-jwt
V2e-jwt

## Slide 13
3. phasors 2 (g)
Phasor domain
Vejωt = (V1 + V2)ejωt ⇒ V = V1 + V2
Im
Re
V1
V2
V

## Slide 14
3. phasors 2 (h)
Time domain
Phasor domain
v (t) = Re[Vejωt] = Re[(V1 + V2)ejωt]

## Slide 15
3. phasors 2 (i)
Re
Im
I
VR
VC = Vo
Vi
Re
Im
I
Vo = VR
VC
Vi
Positive phase shifter
Negative phase shifter