## Slide 1: Recent Progress in Vertical GaN Power Devices (V-GaN) the advantages and applications Compare with Lateral GaN

## Slide 2
Part IV: Future Development of Vertical GaN Devices

## Slide 3
INTRODUCTION: ICNS-15
The ICNS, fully known as the International Conference on Nitride Semiconductors, is one of the most important academic conferences and exhibition events in the field of III-nitride semiconductors.
Held biennially since 1995, the conference focuses on cutting-edge research in materials science, device development, and applications of III-V nitride semiconductors such as gallium nitride (GaN).
It provides a global platform for researchers, scientists, and engineers to exchange ideas, covering the full innovation chain from crystal growth, doping, and heterostructures to optoelectronic devices (e.g., LEDs and lasers) and power electronic devices (e.g., HEMTs).
Five Research Achievements from the GaN Research Group at Shenzhen Pinghu Laboratory Showcased

## Slide 4
INTRODUCTION: vGaN HEMT
On July 10, 2025, Dr. Li Zilan, founder of Guangdong ZIENER, attended the 15th International Conference on Nitride Semiconductors (ICNS-15).
The presentation highlighted the team’s original breakthroughs in silicon-based vertical GaN power devices (vertical GaN HEMTs) and their promising application prospects.
x-SEM structure
Achieve a world-first by directly epitaxially growing a vertical two-dimensional electron gas channel on a silicon substrate.
In terms of process integration, the team achieved a fully vertical electrode layout, which can significantly enhance device heat dissipation efficiency.
Supported by an advanced process platform, this innovative technology exhibits excellent manufacturability for high-volume production.

## Slide 5
INTRODUCTION: vGaN HEMT Technology
Vertical GaN HEMT Power Device Technology

## Slide 6
OVERVIEW: What is vGaN

## Slide 7
OVERVIEW: Science of vGaN

## Slide 8
OVERVIEW: Simple vGaN Structure

## Slide 9
OVERVIEW: vGaN Property
Vertical GaN Properties
Current flows vertically from the bottom to the top surface
Don’t have a 2DEG drain drift region near the surface
Augment the thickness of the N-drift layer
Ability to exhibit avalanche breakdown
Langpoklakpam C, Liu A-C, Hsiao Y-K, Lin C-H, Kuo H-C. Vertical GaN MOSFET Power Devices. Micromachines. 2023; 14(10):1937. https://doi.org/10.3390/mi14101937

## Slide 10
Langpoklakpam C, Liu A-C, Hsiao Y-K, Lin C-H, Kuo H-C. Vertical GaN MOSFET Power Devices. Micromachines. 2023; 14(10):1937. https://doi.org/10.3390/mi14101937
Li, J., Zhu, R., Ming Wong, K., & May Lau, K. (2025). Fully-Vertical GaN-on-SiC Trench MOSFETs. IEEE Electron Device Letters, 46(2), 282–285. https://doi.org/10.1109/led.2024.3520200
‌
OVERVIEW: Vertical Current
Vertical Current Flow Path
Higher Current Density
Carry current through the full thickness of the drift region instead of a thin surface channel
Fully vs. Quasi (Inside vs. Surface)
Reduced current crowding effect allowing more effective scaling of current with the device area
This vertical path reduces series resistance, and enables higher current density, allowing the device to sustain higher breakdown voltage without increasing chip area.
Short current conduction path

## Slide 11
Langpoklakpam C, Liu A-C, Hsiao Y-K, Lin C-H, Kuo H-C. Vertical GaN MOSFET Power Devices. Micromachines. 2023; 14(10):1937. https://doi.org/10.3390/mi14101937
OVERVIEW: Reliability
No 2DEG drain drift region near the surface
High reliability
Electric field and current do not concentrate near the surface
2DEG sensitive
Traps, surface states, dynamic R_ON
Less degradation in dynamic R_ON
Due to trapped impurity charges or
bulk traps resulting from lattice mismatch
This improves stability, reliability, and allows true avalanche behavior
Augment the thickness of the N-drift layer
A low-doped or unintentionally doped GaN epitaxial layer.
This makes the breakdown voltage independent of the lateral size of device.
Ability to exhibit avalanche breakdown
Even distribution of the electric field within the device can mitigate the effects of current collapse by countering the influence of surface states, slowing down the collapse

## Slide 12
OVERVIEW: Advantages

## Slide 13
Langpoklakpam C, Liu A-C, Hsiao Y-K, Lin C-H, Kuo H-C. Vertical GaN MOSFET Power Devices. Micromachines. 2023; 14(10):1937. https://doi.org/10.3390/mi14101937
COMPARISON
Lateral GaN (Si)：
limited performance, with high RON at high voltage and low efficiency.
SiC：
mature and reliable, close to the material limit, suitable for 1–3 kV high-voltage applications.
Vertical GaN：
great potential, with RON close to SiC but still below the GaN theoretical limit.

## Slide 14
COMPARISON: Si/SiC

## Slide 15
COMPARISON: Lateral GaN

## Slide 16
COMPARISON: KEY Difference
Lateral GaN
Because the electric field is concentrated near the surface, it will face premature breakdown when voltage increases
Vertical GaN
Since it spread the electric field across a thick GaN drift layer, allowing them to reach several kilovolts.
Therefore, vertical GaN is more suitable for high-voltage applications like power grids or industrial converters.
The key difference is the current direction
Lateral GaN conducts along the wafer surface (good for low-voltage);
Vertical GaN conducts through the substrate (suitable for high-voltage, high-current);
Vertical GaN offers higher breakdown voltage, lower on-resistance, higher power density, and better heat dissipation;

## Slide 17
SUMMARY
Vertical Current Flow Path
Wide-bandgap semiconductor
Support High Voltage and High Current
High electron mobility and excellent thermal properties
Make GaN Suitable for High-Power and High-Frequency applications
Vertical GaN Devices, the most promising technologies for next-generation power electronics
PV Inverters
Data Center Power Delivery
Industrial Motor Drives
Uniform Bulk Electric Field
Exhibit Avalanche Breakdown

## Slide 18
APPLICATIONS

## Slide 19
APPLICATIONS

## Slide 20
APPLICATIONS

## Slide 21
FUTURE DEVELOPMENT
GaN on GaN:
Using a GaN substrate to fabricate GaN devices, offering better thermal performance and higher voltage tolerance, ideal for high-power and high-frequency applications
GaN on Si:
Integrating GaN devices on a silicon (Si) substrate, combining GaN's high efficiency with silicon's mature manufacturing process, reducing costs and enabling large-scale production
Optical Trigger:
The proposed device was benchmarked against other optical power switches, highlighting its potential in future low-cost, all optical, high-voltage power modules with reduced EMI susceptibility and circuit complexity.
Wrap-Around Gate:
The wrap-around-gate GaN trench CAVETs achieve strong channel control, low leakage, and high breakdown voltage. By tuning groove spacing, both normally-on and normally-off devices are realized, reaching up to 984 V and low specific on-resistance with scalable multi-finger high-current operation.

## Slide 22
FUTURE DEVELOPMENT: GaN on GaN
October 30, 2025
ONSEMI launched 700V/1200V power-semiconductor devices now sampling with early customers;
Targets AI data-centers and EVs, slashes passive-component (caps, inductors) volume, enables 48 V backplane ultra-dense power;
Mass production slated for 2026; market share expected to ramp rapidly;
Application wins
3× power-density boost;
ideal for EV on-board chargers (OBC) and solar inverters;
Challenges
high-cost native GaN substrates;
thermal conductivity still trails SiC;
ONSEMI is a core enabler of global automotive and industrial power and sensing technologies
From Motorola
2016 acquire Fairchild
2025.10

## Slide 23
FUTURE DEVELOPMENT: GaN on GaN

## Slide 24
FUTURE DEVELOPMENT: GaN on Si
Huawei and Shandong University jointly reported FIT-MOS that employs a fluorine-ion-implanted termination (FIT) structure
FIT(Fluorine-ion-implanted)
carries negative fixed charge,
forming a high-resistivity zone that naturally isolates the MOSFET devices
MET(Mesa-etched termination)
electric-field crowding effect at the mesa edges
REPLACE
Y. Ma et al., "1200 V Fully-Vertical GaN-on-Si Power MOSFETs," in IEEE Electron Device Letters, vol. 46, no. 9, pp. 1513-1516, Sept. 2025, doi: 10.1109/LED.2025.3586947.
1277
567
2025.09

## Slide 25
FUTURE DEVELOPMENT: GaN on Si
Y. Ma et al., "1200 V Fully-Vertical GaN-on-Si Power MOSFETs," in IEEE Electron Device Letters, vol. 46, no. 9, pp. 1513-1516, Sept. 2025, doi: 10.1109/LED.2025.3586947.
The fluorine-ion-implanted termination (FIT) technology opens up broad prospects for the application of vertical GaN trench MOSFETs in kilovolt-class power systems.
The breakdown voltage (BV) has been increased from
567 V in the MET-MOS to 1277 V in the FIT-MOS
In addition, the FIT-MOS exhibits
a threshold voltage (Vth) of 3.3 V；
an ON/OFF ratio of 10⁷；
a specific on-resistance (Ron,sp) of 5.6 mΩ·cm²；
an on-state current density of 8 kA/cm²；

## Slide 26
FUTURE DEVELOPMENT: Optcial Trigger
J. -H. Hsia, J. A. Perozek and T. Palacios, "First Demonstration of Optically-Controlled Vertical GaN finFET for Power Applications," in IEEE Electron Device Letters, vol. 45, no. 5, pp. 774-777, May 2024, doi: 10.1109/LED.2024.3375856.
Against other power switches
Tradition
Optical Trigger
Structure
breakdown
2024.05

## Slide 27
FUTURE DEVELOPMENT: Wrap-Around Gate
X. Wen et al., "984V/ 3.0mΩ⋅cm2 Normally-off and 817V/ 2.7mΩ⋅cm2 Normally-on GaN Trench CAVETs With Wrap-Around Gate," in IEEE Electron Device Letters, doi: 10.1109/LED.2025.3631862.
2025.07
S=4μm, on
S=2μm, off

## Slide 28
REFERENCE
[1] Langpoklakpam C, Liu A-C, Hsiao Y-K, Lin C-H, Kuo H-C. Vertical GaN MOSFET Power Devices. Micromachines. 2023; 14(10):1937. https://doi.org/10.3390/mi14101937
[2] Li, J., Zhu, R., Ming Wong, K., & May Lau, K. (2025). Fully-Vertical GaN-on-SiC Trench MOSFETs. IEEE Electron Device Letters, 46(2), 282–285. https://doi.org/10.1109/led.2024.3520200
[3] Y. Ma et al., "1200 V Fully-Vertical GaN-on-Si Power MOSFETs," in IEEE Electron Device Letters, vol. 46, no. 9, pp. 1513-1516, Sept. 2025, doi: 10.1109/LED.2025.3586947.
[4] J. -H. Hsia, J. A. Perozek and T. Palacios, "First Demonstration of Optically-Controlled Vertical GaN finFET for Power Applications," in IEEE Electron Device Letters, vol. 45, no. 5, pp. 774-777, May 2024, doi: 10.1109/LED.2024.3375856.
[5] X. Wen et al., "984V/ 3.0mΩ⋅cm2 Normally-off and 817V/ 2.7mΩ⋅cm2 Normally-on GaN Trench CAVETs With Wrap-Around Gate," in IEEE Electron Device Letters, doi: 10.1109/LED.2025.3631862.

## Slide 29
THANK YOU